## Slide 1
828 m
WIND
TECHNICAL ELEVATION · 163 FLOORS
TECHNICAL DOSSIER · WIND ENGINEERING
Burj Khalifa
Engineering 828 metres against the wind
How aerodynamic shaping, boundary-layer wind-tunnel simulation and a buttressed concrete core produced the world's tallest building.
828m
ARCHITECTURAL HEIGHT
163
FLOORS
27
SETBACKS
40+
WIND-TUNNEL TESTS
TECHNICAL PRESENTATION · OCTOBER 2026
01 / 20
Notes: Opening: Burj Khalifa is not primarily a gravity problem — at 828 m the wind governs. The deck follows the design logic: wind climate, vortex shedding, aerodynamic shaping, wind-tunnel programme, structural response, foundations and verification.

## Slide 2
EXECUTIVE SUMMARY
A 828-metre wind machine — tamed by geometry
02 / 20
THE PROBLEM
At 828 m, wind — not gravity — sets the structural agenda. A slender tower in a 50-year storm meets roughly 43 m/s at the crown; vortex shedding can lock into its first modes and amplify motion.
THE ANSWER
Change the shape at every tier. A Y-plan with 27 spiraling setbacks prevents a coherent vortex street; 40+ tunnel tests and an aeroelastic model verified the response.
828 m
HEIGHT
163
FLOORS
27
SETBACKS
40+
TUNNEL TESTS
1:500
AEROELASTIC SCALE
12 mg
PEAK ACCELERATION
DESIGN OUTCOME
Comfort target
criteria satisfied
0
auxiliary dampers
1.5 m
total sway at the top
22 M
construction man-hours
Sources: SOM; Irwin (CTBUH 2005); Baker et al. (SEI 2015); Novak (ICC 2023). 12 milli-g is the aeroelastic prediction for a 5-year return period.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
02

## Slide 3
WIND STATISTICS
At 828 m, wind becomes the design driver
03 / 20
Chart: 
| 10 | 50 | 100 | 150 | 200 | 300 | 400 | 500 | 600 | 700 | 828
Standard boundary-layer profile | 23.5 | 29.2471 | 32.1369 | 33.958 | 35.3123 | 37.3132 | 38.8013 | 39.9963 | 41 | 41.8682 | 42.835
HEIGHT ABOVE GROUND (m)
MEAN HOURLY WIND (m/s)
THE DESIGN PROFILE
U(z) = U₁₀ · (z/10)^α
α ≈ 0.136 · fitted to the reported 10 m and 600 m values q(z) = ½ ρ U(z)²
50-year return period, mean-hourly — not a 3-second gust.
Mean profile only: gust factors enter in the load cases.
23.5 m/s
50-year mean-hourly wind at 10 m
41 m/s
50-year mean-hourly wind at 600 m
≈ 43 m/s
derived at the 828 m crown
≈ 1.06 kPa
dynamic pressure at the crown
Insight: a 50-year event is not a rare outlier in the design process — it is the load case that sizes the lateral system.
Anchors: Irwin, 'The Wind Engineering of the Burj Dubai Tower' (CTBUH 2005). Curve: power-law interpolation, α fitted to 23.5 m/s at 10 m and 41 m/s at 600 m; dynamic pressure with ρ = 1.15 kg/m³.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
03
Notes: The tower was designed for a 50-year mean-hourly wind of 23.5 m/s at 10 m in open terrain; standard boundary-layer assumptions put the 600 m value at 41 m/s. The top speed is a derived value, not a measured one. The point: the lever arm is enormous even if the wind speed is not.

## Slide 4
AERODYNAMICS
The real enemy: vortex shedding and lock-in
04 / 20
PLAN VIEW · BLUFF BODY IN CROSSFLOW
WIND
TOWER
↻
↺
↻
↺
alternating vortices
f = St · U / D
St ≈ 0.12 · D = plan width resonance when f ≈ structural mode
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
shedding frequency (D = 50 m, St = 0.12) | 0 | 0.012 | 0.024 | 0.036 | 0.048 | 0.06 | 0.072 | 0.084 | 0.096 | 0.108 | 0.12 | 0.132 | 0.144
structural mode (illustrative 0.10 Hz) | 0.1 | 0.1
WIND SPEED U (m/s)
f (Hz)
lock-in ≈ 42 m/s if the mode were 0.10 Hz
Why it matters: a square tower sheds one strong frequency. A tapered, twisted, stepped plan smears that frequency along the height, so no single vortex street can organise.
Physics schematic — not a Burj Khalifa measurement. Shedding relation f = St·U/D with illustrative width and Strouhal number. Shaping strategy: SOM / Irwin (2005).
BURJ KHALIFA · WIND ENGINEERING DOSSIER
04
Notes: Vortex shedding is the crosswind mechanism that governs supertall towers. The chart is a teaching schematic: for a 50 m wide bluff body with St = 0.12 and a 0.10 Hz first mode, lock-in would occur near 42 m/s. Burj Khalifa avoids a single lock-in frequency by changing its plan at every tier.

## Slide 5
MASSING
Confuse the wind: a Y-plan with 27 spiraling setbacks
05 / 20
27 TIERS · EACH ONE A DIFFERENT PLAN
BASE · 0 m
MID · ≈ 300 m
CROWN · ≈ 600 m
THE SHAPING MECHANISM
Three wings set back in sequence — A, then B, then C, clockwise — so the tower presents a different width, depth and corner geometry at every level.
01
No repeating silhouette
The wind never sees the same building twice, so vortices cannot build coherence over height.
02
Width steps down
The plan narrows with height, cutting the reference area that generates crosswind force.
03
Mass follows the moment
Setbacks remove concrete where bending demand is lowest — structure and aerodynamics agree.
The setbacks are aligned to the structural grid: columns above land on walls below, so the shape changes without column transfers.
27 setbacks: SOM and Wikipedia. Wing setback sequence A→B→C and differing plan at each tier: Irwin (CTBUH 2005). Plans are schematic, not construction drawings.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
05
Notes: The Y-plan is the architectural signature, but it is also the aerodynamic device. Each wing sets back in turn, clockwise, changing the plan at every tier. The result is not one vortex street but a stack of different bluff bodies.

## Slide 6
TEST PROGRAMME
Forty-plus tunnel tests, four families of model
06 / 20
TEST MATRIX · INDICATIVE SEQUENCE
CONCEPT
MASSING
FINAL
VERIFY
Aeroelastic
1:500 · dynamics
High-Re
1:50 · sections
Cladding
pressure taps
HFFB
rigid · base force
Dot size = relative weight of that model in each phase. Counts and sequencing are indicative.
RWDI BOUNDARY-LAYER TUNNELS
2.4 × 1.9 m
aeroelastic & cladding
4.9 × 2.4 m
high-Reynolds sections
55 m/s
achievable test speed
PROGRAMME SCALE
40+
TESTS
2
SCALES
3
OUTPUTS
Concept → construction, iterated with SOM.
01
Design loads
Along- and cross-wind base moments for every direction.
02
Occupant comfort
Peak accelerations at the top occupied floor.
03
Cladding pressures
Local peak pressures and suctions for the façade.
Programme facts: RWDI project record; Irwin (CTBUH 2005). Matrix is an explanatory summary, not the project's test log.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
06
Notes: The wind-tunnel programme was not a single test. It ran through the design: massing studies, aeroelastic checks, high-Reynolds sections, cladding pressure mapping and rigid force-balance work. 40+ tests across two RWDI tunnels.

## Slide 7
SIMILITUDE
Reynolds number: the scale that cannot be faked
07 / 20
REYNOLDS SIMILARITY
Re = U · D / ν
ν = 1.5 × 10⁻⁵ m²/s · D = 50 m reference width · U = 40 m/s
FULL SCALE
1.3 × 10⁸
true flow, true aeroelasticity
1:50 SECTION
2.7 × 10⁶
high-Re check on details
1:500 MODEL
2.7 × 10⁵
whole-building dynamics
Bar length ∝ log₁₀(Re). Wind-tunnel Reynolds numbers are 2–3 orders below full scale.
WHY TWO MODEL SCALES?
A full-height 1:50 model would stand 16.6 m tall. So the programme splits the problem: a 1:500 whole-building aeroelastic model captures the dynamic response; 1:50 sectional models push Reynolds number up where corner detail matters.
WHAT CHANGES WITH Re
Sharp corners
insensitive — separation is fixed
Rounded / tapered edges
sensitive — separation moves
Along-wind drag
fairly stable across scale
Cross-wind & torsion
the risk area — needs high Re
Consequence: a 1:500 test alone can mispredict cross-wind force. The 1:50 checks are an insurance policy against scale effects.
Re computed from U = 40 m/s, D = 50 m, ν = 1.5 × 10⁻⁵ m²/s (derived, not reported test values). Model-scale strategy: Irwin (CTBUH 2005); RWDI.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
07
Notes: Reynolds number is the similarity parameter the wind tunnel cannot match. At 1:500 the model is roughly 2.7e5; full scale is 1.3e8. Rounded or tapered corners are Reynolds-sensitive, which is why 1:50 sectional tests were used alongside the whole-building aeroelastic model.

## Slide 8
DYNAMICS
Aeroelastic response: where the tower answers back
08 / 20
Chart: 
REDUCED WIND SPEED Vr = U / (f · D)
NORMALISED RMS TIP RESPONSE
Vr ≈ 8.3
THE LOCK-IN CONDITION
f = St · U / D
Shedding matches a structural mode when Vr = 1 / St ≈ 8.3. A square tower concentrates energy at that one speed; a stepped plan spreads it over 5 < Vr < 14.
AERODYNAMIC DAMPING
Moving air adds damping that grows with speed. It is not a structural damper — it is the wind resisting the tower's own motion. The aeroelastic model captures it; a rigid force-balance test cannot.
damping ratio ∝ ρ U D / (2 m ω)
Read the chart: shaping does not eliminate the dynamic response — it removes the sharp peak that drives the design.
Response curves are a teaching schematic, not measured Burj data. Lock-in condition and Vr = 1/St are standard bluff-body aerodynamics.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
08
Notes: This is the core dynamic argument. A square plan has a narrow, violent lock-in peak near Vr = 8.3. The stepped Y-plan smears that peak across a wide band and lowers its amplitude. Aeroelastic damping — the wind damping the building — is captured only by an aeroelastic model.

## Slide 9
OPTIMISATION
Three numbers: 37 → 19 → 12 milli-g
09 / 20
Chart: 
| Initial massing (May 2003) | After setbacks & taper | Final shape + tuning
value | 37 | 19 | 12
PREDICTED PEAK ACCELERATION · MILLI-g · 5-YEAR RETURN
THE FEEDBACK LOOP
01
Shape
Move the wings, change the setbacks, adjust taper.
02
Test
Aeroelastic model in the boundary layer; directional tests.
03
Compare
Base moments and accelerations against criteria.
04
Refine
Iterate the massing until the response flattens.
−68%
peak acceleration vs the May 2003 baseline
Result: 12 milli-g satisfies the comfort criterion with no auxiliary damping device — mass, stiffness and geometry did the work.
Acceleration history: Irwin (CTBUH 2005); Baker et al. (2015). Values are aeroelastic predictions at the 5-year return period, not measurements.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
09
Notes: The headline of the wind programme: initial predictions were about 37 milli-g, more than twice the comfort target. Setbacks and taper cut it to 19; final geometry and structural tuning brought it to 12 — a 68% reduction without a tuned mass damper.

## Slide 10
OCCUPANT COMFORT
Comfort is a wind-load case too
10 / 20
PEAK HORIZONTAL ACCELERATION · 5-YEAR RETURN PERIOD
IMPERCEPTIBLE
PERCEPTIBLE
RESIDENTIAL TARGET
ABOVE TARGET
UNACCEPTABLE
0
5
10
15
20
25
30
35
40
mg
BURJ 12 mg
TYPICAL 5-YEAR COMFORT TARGETS
Residential
10 – 15 mg
Burj residences & hotel
Hotel
15 – 20 mg
Armani Hotel floors
Office
20 – 25 mg
corporate suites
Observation
25 – 30 mg
At the Top decks
Limits are frequency-dependent and project-specific; the bands above are typical supertall practice, not code minima.
WHY 12 MILLI-G IS THE RIGHT NUMBER
■
Damping is structural
Concrete core, finishes and foundations give roughly 1–2% of critical — the model must assume the low end.
■
No damper, no fallback
Without a TMD, the margin has to come from geometry and stiffness. 12 mg leaves room for uncertainty.
■
Serviceability, not safety
Comfort governs the 5-year storm; strength is governed by the 50-year load case.
12 mg: aeroelastic prediction for the 5-year return period (Irwin 2005; Baker et al. 2015). Comfort-band thresholds are illustrative of ISO 10137 practice.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
10
Notes: Comfort is a serviceability limit state checked at the 5-year storm, not the 50-year strength case. The design target sits inside the residential band, which is why 12 milli-g mattered. With no auxiliary damper, that margin had to be bought with shape and stiffness.

## Slide 11
STRUCTURAL SYSTEM
The buttressed core: three wings holding each other up
11 / 20
PLAN · TYPICAL FLOOR · SCHEMATIC
WING A
WING B
WING C
CORE
WIND
Each wing braces the other two. Remove one and the system loses its torsional stiffness.
HOW A BUTTRESSED CORE WORKS
A central hexagonal hub with three residential wings. The wings are not attached decoration — they are the lateral system. Wind on one wing is resisted by the other two acting as buttresses.
■
Torsion
Wings at 120° put mass and stiffness away from the centre, raising torsional resistance.
■
Overturning
The plan spreads compression over a wide footprint, cutting foundation pressure.
■
Flexibility
Wall lengths set the period — long wings are stiff in bending but never fully closed.
C60 – C80
high-strength concrete in the walls and core
3 wings · 1 core
no perimeter moment frame
Buttressed-core concept and concrete grades: SOM / Baker et al. Plan is a schematic, not a construction drawing.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
11
Notes: The buttressed core is the structural idea that makes the Y-plan work. Three wings around a hexagonal hub: each wing buttresses the other two, giving torsional stiffness without a perimeter frame. The same geometry that confuses the wind also carries the load.

## Slide 12
LOAD PATH
From wind pressure to the ground in five steps
12 / 20
ELEVATION · OUTRIGGER LEVELS
01
02
03
04
05
WIND
5 outrigger sets
Chart: 
| 1.0 | 0.9506249999999999 | 0.9025 | 0.8556250000000001 | 0.81 | 0.765625 | 0.7224999999999999 | 0.6806249999999999 | 0.6400000000000001 | 0.6006250000000001 | 0.5625 | 0.525625 | 0.48999999999999994 | 0.45562500000000006 | 0.42250000000000004 | 0.390625 | 0.36 | 0.33062499999999995 | 0.30250000000000005 | 0.275625 | 0.25 | 0.225625 | 0.20249999999999996 | 0.18062500000000004 | 0.16000000000000003 | 0.140625 | 0.12249999999999998 | 0.10562499999999997 | 0.09000000000000002 | 0.07562500000000001 | 0.0625 | 0.05062499999999999 | 0.03999999999999998 | 0.030625000000000017 | 0.022500000000000006 | 0.015625 | 0.009999999999999995 | 0.005624999999999994 | 0.0025000000000000044 | 0.0006250000000000011 | 0.0
overturning moment | 0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5 | 0.525 | 0.55 | 0.575 | 0.6 | 0.625 | 0.65 | 0.675 | 0.7 | 0.725 | 0.75 | 0.775 | 0.8 | 0.825 | 0.85 | 0.875 | 0.9 | 0.925 | 0.95 | 0.975 | 1
M / M_base
z / H
WHY OUTRIGGERS?
They couple the core to the perimeter columns, widening the effective structural depth. Five sets keep the core from carrying the whole moment alone.
Load path: façade → floor plates → core walls → outriggers → columns → raft → piles.
Outrigger sets and load path: SOM / Baker et al. (2015). Moment curve is the elastic cantilever relation M(z) ∝ (H − z)², normalised.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
12
Notes: The outriggers are the load-path shortcut. Instead of the core alone resisting overturning, five sets of outrigger walls engage the perimeter columns and widen the structural depth. The moment diagram shows why the base is the expensive part.

## Slide 13
FOUNDATIONS
192 piles, one raft, and a lot of Dubai sand
13 / 20
SECTION · PILED RAFT · SCHEMATIC
SAND / WEAK ROCK
CALCARENITE
BEARING STRATUM
TOWER ABOVE
192 piles · spacing schematic
3.7 m raft
47.45 m
THE NUMBERS
192
bored piles
1.5 m
pile diameter
47.45 m
pile depth
3.7 m
raft thickness
WHY A PILED RAFT?
Dubai's ground is weak carbonate sand and rock. The raft spreads load; the piles reach the stronger stratum and mobilise skin friction. Excavating the basement also removes weight — a compensated foundation, so the net pressure on the soil stays low.
Net pressure ≈ building weight − excavated soil
Pile count, diameter, depth and raft thickness: CTBUH / SOM foundation papers. Section is diagrammatic; pile spacing is not to scale.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
13
Notes: The foundation is a piled raft: a 3.7 m raft on 192 bored piles, 1.5 m diameter and about 47 m deep. The basement excavation is part of the design — removing soil weight compensates for the tower, so net ground pressure stays manageable.

## Slide 14
CONSTRUCTION
Building 828 metres, one climbing cycle at a time
14 / 20
330,000m³
concrete
39,000t
reinforcement
C60–C80
concrete cube strength
22 M
construction man-hours
12,000
workers at peak
600 m+
concrete pump height
THE CLIMBING SYSTEM
A self-climbing formwork system jumped with the core. Each wing followed its own cycle, so the setbacks were built as ordinary floor steps — no transfer beams, no temporary works holding the shape.
CORE
leads
WINGS
follow
SETBACKS
stack
PROGRAMME · 2004 – 2010
2004
Excavation and piling
192 piles; 3.7 m raft cast in stages.
2005
Tower rises
Climbing formwork established; core leads the wings.
2007
Level 100
Concrete pumped beyond 400 m — a record at the time.
2009
Topped out
Spire completes at 828 m; cladding closes.
2010
Opening
Burj Khalifa opens on 4 January.
Why it matters: the aerodynamic shape had to be buildable. A geometry that saves wind load but adds a transfer structure would have lost the argument.
Quantities: SOM / CTBUH project records; ICC Building Safety Journal (2023). Programme dates are approximate milestones.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
14
Notes: Construction is where the aerodynamic argument meets logistics. 330,000 cubic metres of concrete, 39,000 tonnes of steel, 22 million man-hours. The setbacks were aligned to the structural grid so the shape could be built with a climbing formwork cycle, not special transfers.

## Slide 15
VERIFICATION
Five models, one building: the simulation stack
15 / 20
01
Climate
Met data, balloon profiles, MM5 mesoscale modelling → design speed profile.
→ design wind profile
02
Shape
Massing studies; setbacks and taper iterated against aerodynamic response.
→ candidate massing
03
Tunnel
1:500 aeroelastic + 1:50 high-Re + cladding pressure tests.
→ loads & accelerations
04
FE model
Shell model of core, wings, outriggers; mode shapes and periods.
→ stresses & drift
05
Design
Load cases, reinforcement, comfort check, foundation design.
→ construction drawings
CROSS-CHECKS · NO SINGLE MODEL DECIDES
CFD
pressure fields, qualitative
Aeroelastic
dynamic response + damping
HFFB
base moments, many directions
FE
internal forces, drift, periods
Four independent checks. A disagreement is a design flag, not a rounding error.
THE RULE
Wind tunnel gives the loads. Finite element gives the stresses. Neither is trusted alone — the design only closes when both agree.
If they disagree, re-test the geometry — don't average the answer.
Practical point: the models were updated as the massing changed. A wind tunnel result is only valid for the geometry that was tested.
Workflow reconstructed from published project papers (Irwin 2005; Baker et al. 2015; RWDI). Tool names are not claimed.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
15
Notes: Five models, not one. Climate gives the input, shape studies narrow the options, the tunnel measures the loads, the finite-element model turns loads into stresses, and the design closes the loop. Each model checks the others.

## Slide 16
MONITORING
The tower as a full-scale experiment
16 / 20
INSTRUMENTATION · SCHEMATIC
GPS + anemometer
top displacement & wind speed
accelerometers
3 levels, two axes
strain gauges
core & outrigger walls
temperature
thermal gradients
Sensors validate the models, not just the building: measured frequencies and damping feed back into the next design.
Chart: 
TIME HISTORY · ≈ 0.11 Hz FIRST MODE
MILLI-g
WHAT THE DATA PROVED
Frequencies
measured modes landed close to the FE predictions — the stiffness model was right.
Damping
roughly 1–2% of critical, amplitude-dependent; the low end governed the design.
Response
measured accelerations stayed inside the wind-tunnel envelope.
Monitoring scope: published SHM descriptions (SmartSync / CTBUH). Time history is an illustrative 10-minute record, not measured Burj data.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
16
Notes: The building itself is the last model. Accelerometers, GPS, anemometers and strain gauges check the assumptions: frequency, damping, and the actual acceleration envelope. Measured damping of 1–2% is why the design cannot rely on a high damping assumption.

## Slide 17
SCORECARD
Did the design deliver what it promised?
17 / 20
Metric | Design intent | Verified outcome | Status
Height | 828 m architectural | 828 m, 163 floors | MET
Design wind | 50-yr mean-hourly, 23.5 m/s @ 10 m | 41 m/s at 600 m, ≈43 m/s at crown | ADOPTED
Comfort | ≤ 15 milli-g, 5-yr return | 12 milli-g predicted | MET
Damping devices | avoid auxiliary dampers | none installed | MET
Top sway | ≈ 1.5 m in the design storm | within serviceability limits | MET
Foundation | piled raft on 192 piles | 192 × 1.5 m, 47.45 m deep, 3.7 m raft | MET
Wind tunnel | 40+ tests, two scales | 1:500 aeroelastic + 1:50 high-Re | MET
Occupancy | mixed-use, 163 floors | residential, hotel, office, observation | OPENED 2010
THE HEADLINE
−68%
peak acceleration versus the first massing study — without a damper.
THE CAVEAT
Acceleration and sway are predictions, not long-term measurements. The scorecard marks design intent, not proof.
Long-term monitoring, a stronger storm or added damping would update the verdict.
Table compiled from SOM, RWDI, CTBUH and ICC sources. 'MET' = design target reported as satisfied; acceleration values are aeroelastic predictions.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
17
Notes: The scorecard is deliberately conservative: it separates what was designed from what was measured. The 68% acceleration reduction and the no-damper outcome are the headline. The caveat matters — comfort numbers are predictions.

## Slide 18
LESSONS
Six principles that transferred beyond Dubai
18 / 20
01
Shape before stiffness
Geometry removed 68% of the acceleration. Adding concrete would have cost far more.
37 → 19 → 12 milli-g
02
Test the dynamics
An aeroelastic model captures damping and lock-in; a rigid pressure test cannot.
1:500 model · 40+ tests
03
Let structure follow wind
Setbacks aligned to the column grid: the aerodynamic move was also the structural move.
27 setbacks · no transfers
04
Design the margin
No damper meant the shape and stiffness had to carry the uncertainty.
12 mg with 0 dampers
05
Verify at two scales
Reynolds effects are real; the 1:50 checks are cheap insurance.
1:50 sections vs 1:500
06
Design for the occupant
Comfort, not code minimum, sized the top of the tower.
12 mg vs 10–15 mg target
The transferable idea: at supertall height, the cheapest structural material is the shape of the building.
Synthesis of published Burj Khalifa wind-engineering papers; principles are the author's interpretation, not a client statement.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
18
Notes: Six transferable principles. The strongest is the first: shape is cheaper than stiffness. The rest are process lessons — test dynamics, align architecture with structure, keep margin, verify at two scales, design for people.

## Slide 19
AEROELASTIC SAFETY
Five instabilities a supertall must survive
19 / 20
Instability | Mechanism | Burj Khalifa response
Vortex shedding | Alternating vortices create a cross-wind force at the shedding frequency. | Stepped Y-plan smears the frequency; no coherent lock-in over the full height.
Lock-in | Shedding synchronises with a structural mode and amplifies motion. | 27 setbacks and taper keep the response broad and low.
Galloping | Negative aerodynamic damping drives divergent cross-wind oscillation. | Bluff, stiff concrete section; no slender icy cables or sharp-section galloping.
Flutter | Coupled torsional–translational instability above a critical wind speed. | High torsional stiffness from the three-wing core; design speed well below critical.
Wake buffering | Downstream towers sit in another building's wake. | Site layout and directionality considered in the tunnel programme.
Key point: comfort and safety are different checks. Comfort is a 5-year acceleration limit; safety is the 50-year strength and stability case.
Instability definitions: standard bluff-body aeroelasticity. Burj responses are qualitative summaries of the published shaping strategy.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
19
Notes: Five instabilities, one shape response. Vortex shedding and lock-in are the design drivers; galloping and flutter are checked and kept far from the design speed. Wake buffering matters because Dubai Marina grew up around the tower.

## Slide 20
SOURCES & METHOD
What is measured, what is modelled, what is schematic
20 / 20
PRIMARY SOURCES
Irwin, P. A.
'The Wind Engineering of the Burj Dubai Tower', CTBUH 2005.
Baker, W. F. et al.
'The Structural Design of the World's Tallest Structure', SEI 2015.
RWDI
Project record: Burj Khalifa wind tunnel testing.
SOM
Burj Khalifa project documentation.
ICC Building Safety Journal
'A Tall Adventure', 2023.
CTBUH
Height criteria and project data.
HOW TO READ THE NUMBERS
REPORTED
828 m, 163 floors, 192 piles, 40+ tests, 23.5 m/s at 10 m.
PREDICTED
12 milli-g, 37 → 19 → 12, 1.5 m top sway.
DERIVED
α ≈ 0.136, 43 m/s at the crown, Reynolds numbers.
SCHEMATIC
lock-in curves, moment diagram, foundation section.
Burj Khalifa
Wind engineering dossier · 20 slides
Aerodynamic shape, verified by simulation, built in concrete.
Prepared as a technical explainer. No confidential project data is included.
BURJ KHALIFA · WIND ENGINEERING DOSSIER
20
Notes: Close on method: separate reported facts from predictions, derived quantities and teaching schematics. The deck's argument is that the shape did most of the engineering work — and the test programme proved it.